2. details for the logic blocks in L2 Cache

tag_load_logic
This block is a decoder that if the input load signal is high, it output one of the tag_load signal to be high, according to LRU. Other signals will be low.

data_load_logic
This block is a decoder that if the first bit of the load_data_select is high, then depending the second bit, the block will raise the corresponding output signal accroding to hit_way or

Inputs signals	Outputs signals	logics
LRU(logic) / hit_way(logic) / load_data_select(logic[1:0])	data_1_load(logic) / data_2_load(logic)	data_1_load=0; / data_2_load=0; / if (load_data_select ==0b10) { / if (hit_way==0b0) / data_1_load=1; / else / data_2_load=1; / } else if (load_data_select==0b11) { / if (LRU==0) / data_1_load=1; / else / data_2_load=1; / }

valid_load_logic
This block contains two AND gates and one NOT gate. The first AND gate’s inputs are set_valid and the signal LRU gone by the NOT gate, namely !LRU, and its output is valid_1_load. The second AND gate does the logic and between set_valid and LRU and outputs to valid_2_load signal.

Inputs signals	Outputs signals	logics
LRU(logic) / set_valid(logic)	valid_1_load(logic) / valid_2_load(logic)	valid_1_load=0; / valid_2_load=0; / if (set_valid==0b1 && LRU==0) / valid_1_load=1; / else (set_valid==0b1 && LRU==1) / valid_2_load=1;

dirty_load_logic
To use less logic as possible, the dirty_1_in and dirty_2_in can be directly connect to the set_dirty signal. To generate the dirty_1_load and dirty_2_load, we need 4 3-to-1 AND gates, 2 OR gates, and 6 NOT gates. To output the dirty_1_load signal, we use 2 3-to-1 AND gates, 1 OR gate and 4 NOT gates to complete the following logic:
(!hit_way)*set_dirty*(!clr_dirty)+(!LRU)*(!set_dirty)*clr_dirty
To generate the signal dirty_2_load, we use the rest of the logic gates to do the following logic:
hit_way*set_dirty*(!clr_dirty)+LRU*(!set_dirty)*clr_dirty

Inputs signals	Outputs signals	logics
LRU(logic) / clr_dirty(logic) / set_dirty(logic) / hit_way(logic)	dirty_1_load(logic) / dirty_2_load(logic) / dirty_1_in(logic) / dirty_2_in(logic)	dirty_1_load=0; / dirty_2_load=0; / dirty_1_in=0; / dirty_2_in=0; / if (set_dirty==0b1){ / if (hit_way==0){ / dirty_1_load=1; / dirty_1_in=1; / } / else { / dirty_2_load=1; / dirty_2_in=1; / } / } / else if (clr_dirty==0b1) { / if (LRU==0) / dirty_1_load=1; / else / dirty_2_load=1; / }

pmem_addr_logic
We use two 2-to-1 MUX with data-width of 32 bits. We use LRU to select {tag_1_out[23:0],set[2:0],5’b0} by LRU as one, and {tag_2_out[23:0],set[2:0],5’b0} with LRU being zero. Then we use pmem_addr_select to select {mem_addr[31:5] , 5’b0} as pmem_addr being zero, and the output from the previous MUX by pmem_addr_select as one.

Inputs signals	Outputs signals	logics
set(logic [2:0]) / LRU(logic) / tag_1_out(logic[23:0]) / tag_2_out(logic[23:0]) / mem_addr(logic[31:0]) / pmem_addr_select(logic)	pmem_addr(logic[31:0])	pmem_addr={mem_addr[31:5], 5’b0}; / if (pmem_addr_select==1){ / if (LRU==0) / pmem_addr={tag_1_out[23:0],set[2:0],5’b0}; / else / pmem_addr={tag_2_out[23:0],set[2:0],5’b0}; / }

mem_data_convertor
This block contains two 32-to-1 MUX and one 2-to-1 MUX, and both of the MUXs’ data-width are 32 bit-long. The selecting bits are {offset, byte_offset} for the 32-to-MUX. The 32 inputs for each this MUX is either 32 continuous logic signals from data_1_out with stride of 1 bit or from data_2_out. Note that the out-of-boundary bits are hardcode to zero. The other 2-to-1 MUX then select from the two outputs by hit_way. hit_way equal to zero makes to select data_1_out’s output, and hit_way equal to one makes to select data_2_out’s output.

Inputs signals	Outputs signals	logics
data_1_out(logic[255:0]) / data_2_out(logic[255:0]) / offset(logic[2:0]) / byte_offset(logic[1:0]) / hit_way(logic)	mem_rdata(logic[31:0])	if(hit_way) / { / if(offset==7 && byte_offset!=0) { / case(byte_offset) / 2'b01: / mem_rdata={8'b0, data_2[31-:24]}; / 2'b10: / mem_rdata={16'b0, data_2[31-:16]}; / 2'b11: / mem_rdata={24'b0, data_2[31-:8]}; / default / mem_rdata=32'b0; / endcase / } / else / mem_rdata=data_2[(32*offset+8*byte_offset+31)-:32]; / } / else { / if(offset==7 && byte_offset!=0) { / case(byte_offset) / 2'b01: / mem_rdata={8'b0, data_1[31-:24]}; / 2'b10: / mem_rdata={16'b0, data_1[31-:16]}; / 2'b11: / mem_rdata={24'b0, data_1[31-:8]}; / default / mem_rdata=32'b0; / endcase / } / else / mem_rdata=data_1[(32*offset+8*byte_offset+31)-:32]; / }

datain_logic
This block contains one 2-to-1 MUX with data-width of 256 and 256 5-to-1 MUX, whose outputs will concatenate to the mem_wdata_out. The first MUX will use hitway to select 256-bit signal either from data_1_out(hitway==0) or data_2_out(hitway==1). For description reason, let us divide the mem_wdata_out signals to 32 8-signal groups, and within each group the 8 signals are continuous and have order from 1 to 8. The input signals to the MUX that generates the signal of a certain group with certain number, ie 1st group 2nd signal, are related to its signal numbers, ie 2 here. Let us also divide the mem_wdata to 4 8-signal groups. The five inputs to the MUX are then the 4 signals in the mem_wdata with different group number but same signal number and also the signal with the same position from the output of the 2-to-1 MUX selected by hitway. The selecting bits for these 256 MUX satisfies such a way that if the bit number of output are small than #(32*offset+8*byte_offset) or greater than #(32*offset+8*byte_offset+31), then select the output signals from the previous MUX. Otherwise, select the signals in the mem_wdata_out within all the group number that is equal to #({offset, byte_offset}+offset from mem_byte_enable) to be the mem_wdata signals with the corresponding signals that falls in the all group number #(offset from mem_byte_enable).

Inputs signals	Outputs signals	logics
mem_wdata(logic[31:0]) / mem_byte_enable(logic[3:0]) / offset(logic[2:0]) / hitway(logic) / data_1_out(logic[255:0]) / data_2_out(logic[255:0])	mem_wdata_out / (logic[255:0])	if(hit_way) / mem_wdata_out[255:0]=data_2[255:0]; / else / mem_wdata_out[255:0]=data_1[255:0]; / if(mem_byte_enable[0]) / mem_wdata_out[(32*offset+8*byte_offset+7)-:8]=mem_wdata[7:0]; / if(mem_byte_enable[1]) / mem_wdata_out[(32*offset+8*byte_offset+15)-:8]=mem_wdata[15:8]; / if(mem_byte_enable[2]) / mem_wdata_out[(32*offset+8*byte_offset+23)-:8]=mem_wdata[23:16]; / if(mem_byte_enable[3]) / mem_wdata_out[(32*offset+8*byte_offset+31)-:8]=mem_wdata[31:24];

hit_checker
This block contains two comparator(24-bit data width) and one 2-to-1 MUXs(1-bit long). The two comparators compare the mem_addr[31:8] with tag_1_out and mem_addr[31:8] with tag_2_out respectively. The two 1-bit outputs then come into OR gate and generate the hit signal. To simplify the logic, hit_way logic can be connected to the output signal from the comparator comparing tag_2_out and mem_addr[31:8] signals.

Inputs signals	Outputs signals	logics
tag_1_out(logic[23:0]) / tag_2_out(logic[23:0]) / valid_1_out(logic) / valid_2_out(logic) / mem_addr[31:8](logic[31:0])	hit(logic) / hit_way(logic)	hit=0; / hit_way=0; / if (tag_1_out==mem_addr[31:8] && valid_1_out==1) / hit=1; / else if (tag_2_out==mem_addr[31:8] && valid_2_out==1) { / hit=1; / hit_way=1; / }